## Slide 1: EMBEDDED SYSTEMS PROJECTS

## Slide 2: TEAM PRESENTATION:
PAMIDI MOHAMMAD ASHRAF
S20210020303
SANDEEP NIDAMANURI
S20210020300
PRAVEEN KUMAR
S20210020313
J MOHIT NAGA VARDHA GANESH
S20210020283

## Slide 3: 1 Wireless Stethoscope
Let’s start with the first set of slides

## Slide 4: Most heart diseases are associated with and reflected by the sound that the heart produces, and one of the easiest and cheapest ways of diagnosing cardiac dysfunction is by Heart auscultation i.e. listening to the heart sound. Now if we are talking about traditional auscultation, that requires experience and good listening skills. That is why in this project we thought to build an electronic stethoscope that will be able to get the heart rate of the human body and we can display the data in a Bluetooth-based serial terminal window.
ABSTRACT:

## Slide 5: In this project the heart rate of the subject is been converted into electrical signals. These sound waves of the patient is being recorded through the microphone and this microphone helps the sound waves which enter into the control board. These sound waves are amplified using amplifier. Those amplified signal is sent to the controller. The controller has the code where we can determine the electrical signal’s heart rate. Arduino uno sends the signal to the Bluetooth where it can be controlled by any android or iOS device where the output can be seen in the respected device. In traditional stethoscope, the noise can be arise due to the patients dress or any other obstruction which is rectified using the amplifier in our project where the noise and the artifact can be removed and rectified for the clear heart rate.
JUSTIFICATION:

## Slide 6: BLOCK DIAGRAM:
Arduino UNO
Bluetooth Module
Stethoscope chest piece
Power supply (lithium battery)
Microphone
Android UI
Amplifier
Low Pass filter

## Slide 7: COMPONENTS:
HARDWARE | SOFTWARE
Arduino UNO Bluetooth Module HC-05 LM393 Analog Comparators Breadboard Lithium battery/ 9V battery Stethoscope chest piece Medical grade tube Jumper Wires Plugin microphone | Arduino IDE Bluetooth interface App/Web interface

## Slide 8
Phase-I: Outputs for pre-evaluation –
              Implementing the wireless stethoscope which checks and
              gives the heart rate.
Phase Wise Implementation:
Phase-II: Outputs for final evaluation –
Implementing the wireless stethoscope which will be capable for user interface.

## Slide 9: 2 SECURITY BAND

## Slide 10: Nowadays the safety of a person has become a big question mark. A personal safety/security threat is defined as a situation which may be in the form of an assault, sexual assault, assault causing bodily harm, threat of assault, uttering threats of death/damage, harassment (criminal) of an individual or any other act that constitutes a violent act. Most of the cases you can call for help through your mobile phone but in some difficult situations you can't do it. So we have come up with an idea to improve the security of people so that by simply pressing a button or by shouting loudly you can avoid the insecure situations. This report describes the implementation of security band, what are modules used ,block diagram etc.
ABSTRACT:

## Slide 11: This project provides or helps to establish the communication between the police/hospitals/guardians by an easy procedure. This project has a very simple set of instructions so that all kinds of people (from kids to old people) can Operate and use it without any problem. Using this security band we can establish a safe and secure community.
JUSTIFICATION:

## Slide 12: BLOCK DIAGRAM:
GPS
module
Arduino
nano
Power supply
Pulse rate sensor
Sound sensor
GSM module
Lithium battery
Battery charging module
Andriod message interface

## Slide 13: COMPONENTS:
HARDWARE | SOFTWARE
Arduino nano Switch Resistors Battery charging module tp4056 GPS module noe6m GSM module sim800L Lithium battery 3.7 volt Pulse sensor (Heart beat) PCB board Jumper wires Batteries (Rechargable) Andriod messages | Arduino IDE SMS alert GPS interface

## Slide 14
Phase-I: Outputs for pre-evaluation –
Demonstration of sending message alert to the phone using the switch in the Arduino board using the sim module
Phase Wise Implementation:
Phase-II: Outputs for final evaluation –
Demonstration of sending message alert to the mobile phone using both the switch and the mic sensor using the sim module.

## Slide 15: 3 FIRE FIGHTING ROBO CAR

## Slide 16: In real life, fire accidents can happen anytime and anywhere that usually are hardly controllable. According to National Crime Records Bureau (NCRB), it is estimated that more than 1.2 lakh deaths have been caused because of fire accidents in India from 2010-2014. Even though there are a lot of precautions taken for Fire accidents, these natural/man-made disasters do occur now and then. In addition, death not only due to the fire but also from smoke inhalation and toxic gases. Therefore the fire security is important to human life. The primary duty of fire fighters is to handle fire incidents, which often exposed them to high risks when carrying out the task of extinguishing fire, especially in hazardous area. With the advancement of technology especially in Robotics it is very much possible to replace humans with robots for fighting the fire. Therefore, designing an automatic firefighting robot which will automatically sense the fire and start the water pump will be a good idea. This would improve the efficiency of firefighters and would also prevent them from risking human lives.
ABSTRACT:

## Slide 17: This project presents the development of a fire extinguishing robot with SMS alert feature. When the flame sensors detected the fire, the robot will move to the fire source and send a warning message to the user. Once the robot reached the burning area, it will stop at a certain distance and extinguish the fire by using water.The Arduino Uno can be programmed using Arduino IDE. By this idea we can prevent firefighters from risking their lives and can quickly save human lives from these big disasters. This developed autonomous system demonstrates capabilities of identifying fire locations automatically and extinguishes the fire using the stored mixture in the container placed on it.
JUSTIFICATION:

## Slide 18: BLOCK DIAGRAM:
ARDUINO UNO
L293D
MOTOR
DRIVER
LEFT
DC
MOTOR
RIGHT
DC
MOTOR
POWER
SUPPLY
SIM 800L
LM2956
MQ2
SERVO
MOTOR
FLAME
SENSOR
RIGHT
FLAME
SENSOR
LEFT
FLAME
SENSOR
CENTRE
POWER
SUPPLY
POWER
SUPPLY
WATER
PUMP
RELAY
MODULE
Bluetooth module

## Slide 19: COMPONENTS:
HARDWARE | SOFTWARE
ARDUINO UNO SIM 800L FLAME SENSOR MQ2 SENSOR L293 MOTOR DRIVER RELAY MODULE LM 2596 BUCK CONVERTOR SERVO SG 90 MINI WATER PUMP(5V) BO MOTOR WHEEL (X4) 18650 BATTERY (X3) BREAD BOARD JUMPER WIRES | Arduino IDE Application interface SMS alert

## Slide 20
Phase-I: Outputs for pre-evaluation –
Implementation of the fire fighting robot which will automatically sense the fire/smoke and starts the water pump.
Phase Wise Implementation:
Phase-II: Outputs for final evaluation –
        Implementation of the fire fighting robot with user controlled app interface and SMS alert feature.

## Slide 21: 4 SMART WALKING CANE

## Slide 22: Navigation is unavoidable for humans. The challenging task for blind or poor visibility people is moving from one place to another independently. Travelling in unfamiliar environment without fellowship is harmful for blind or poor visibility people. It is also essential to know the whereabouts of blind or poor visibility people by caretaker when travelling alone. Sight is very important of the five senses. Low vision or blindness has a long-lasting effect on all aspects of an individual’s life. They have to rely on others for helping them in their day to day lives like transportation, shopping, academics, and other chores. In this research paper, the existing work in the field of navigation for blind people is discussed based on which a guidance system solution is proposed for people suffering from complete or partial vision loss. The proposed systems based on the concepts of the Internet of Things.
ABSTRACT:

## Slide 23: The goal of the smart cane is to bring the walking cane up to technological modernity while maintaining its affordable price. The Smart Cane is geared towards an elderly, less affluent demographic group that would demand comfort, accessibility, and affordability from the product. Using the ultrasonic sensor, Arduino board, and vibration motor, the Smart Cane greatly increases the object detection range of the walking cane, thereby improving the lives of the visually impaired users. Also the GSM-GPS technology used in the system provides security during emergency situations. Overall, the use of technology provides much more benefits than the walking cane, and has taken a great leap towards improving the lives of the visually impaired. We seek in our project to provide a smart stick affordable and suitable for most blind people, and it is light in weight. It can be made available to all segments of the society and their families who need them.
JUSTIFICATION:

## Slide 24: BLOCK DIAGRAM:
ULTRASONIC SENSOR
PUSH BUTTON
SIM MODULE
GPS MODULE
LM2596 converter
RAIN DROP SENSOR
ARDUINO NANO
Power supply
BUZZER

## Slide 25: COMPONENTS:
HARDWARE | SOFTWARE
Two ultrasonic sensors Rain drop sensor Push button Arduino Nano microcontroller NEO – 6M GPS Module SIM800L GSM Module LM2596 Converter 9V Battery Walking cane | Arduino IDE GPS interface SMS alert

## Slide 26
Phase-I: Outputs for pre-evaluation –
Implementing the walking cane with obstacle detection, push button and water sensor.
Phase Wise Implementation:
Phase-II: Outputs for final evaluation –
Implementing the walking cane with addition of GPS location tracker and SMS alert.